SAD PROJECT
Spacecraft
- 6U cubesat HYPSO-1
- Inertia matrix (generated from ChatGPT): J = diag([​0.0823, 0.0633, 0.0317)] kg/m^2
- Dimensions (lx, ly, lz) : 10 cm x 20 cm x30 cm
- Mass: 7.6 kg
- NORAD catalogue number: 51053

Orbit https://celestrak.org/NORAD/elements/table.php?INTDES=2022-002&SHOW-OPS
- Period T = 93.91 min
- Inclination i = 97.36 deg
- Semi-major axis a = 6844 km
- Perigee rp = Re + 469.3 km = 6840.3 km
- Apogee ra = Re + 476.9 km = 6847.9 km
- Eccentricity e = 0.0005568

Pointing -> EARTH POINTING
Earth pointing adapts well to our kind of orbit but if we want to do this kind of pointing it will be smart to have horizon sensor (we don’t have it). We can justify the use of gyro bc with only horizon sensor we cannot detumble in eclipse only with that.
In this way we have to use only sun sensor + gyro? We can justify magnetometer presence bc we can use b_dot law for detumbling (search it!).
We could also do sun pointing.
Another option is inertial pointing.
The pointing will be inside REQUIRED ATTITUDE.

Attitude determination
Implement algebraic method, then try to implement statiscal methods and compare them.
Also for attitude determination we have to decide if we want to use SUN SENSOR + GYRO only or SUN SENSOR + GYRO + MAGNETOMETER (when in eclipse gyro + magnetometer, when in the Sun no gyro). These are only ideas. If we have time we can also compare these two options and choose the better one.

FOR NEXT THURSDAY
PRIORITY
- CMG model (actuator) implementation
- Air drag model
- b_dot
- PID
- Optimal observer
NON-PRIORITY
- Migrating the model into CUBESAT
- Improve the plots
- Compare perturbances
- Magnetometer disturbances on every component separatedly

DETUMBLING -> b_dot control law or w_dumping
SLEW MANEUVER -> One of Lyapunov pre-made V (with quaternions)
POINTING -> implement both PID and optimal observer